## Slide 1: Cycle to Cycle Clustering preliminary report
Shuheng Liu

## Slide 2: Motivation
In TCCIII engine data set, hundreds of cycles are measured, including flow feature evolution and pressure signal.
Is there a way to sort out flow features into groups so that we can simplify the description?
How can we find out the most and the least deviated cycle? Can deviation of cycles be quantified?
Can flow feature be predicted by just monitoring pressure signal?

## Slide 3: Idea to answer
crank angle/ time
possible flow features
-Every black dot is a flow feature, in clustering, we call it centroid.
-Every cycle can be represented by a line path in the network, for instance, the red line path.
Discritization in time
Discritization in flow feature
-The simplification comes from discritization in both time and flow feature

## Slide 4: How to get the discritized flow features(black dots)
Through unsupervised machine learning techniques: Clustering
Widely used clustering techniques: kmeans, spectral clustering
Function: Assign flow features to clusters and derive the centroid of each cluster.
For example, in 2D space, there are a bunch of data points(Flow features are just data points in very high dimension), scattered in an xy coordinate system, these data can be put into 2 or 3 clusters. Number of clusters can be decided by users.

## Slide 5: How to get the discritized flow features(black dots)
-After kmeans, resulting clusters and centroids are shown below:

## Slide 6: How to quantify the deviation of centroids
After clustering on all the flow features at interesting crank angles, there is a probability distribution for every interesting crank angle θ1,θ2,...,θNθ, recorded by a probability distribution vector . For example, yi1 is number of flow features in cluster1, normalized by total number of flow features at i th interesting crank angle.
To quantify how much centroid j deviates from mean of crank angle i, we compute distance hji between yi and the exact distribution, for example .
crank angle/ time
possible flow features
crank angle/ time
deviation

## Slide 7: How to quantify deviation of cycles
-According to the line path of each cycle, a so-called distance evolving matrix H can be assembled:
-The ith row of H contains the h sequence of the i th cycle.
crank angle/ time
possible flow features
crank angle/ time
deviation
-The significance of H: H contains the deviation information of all the cycles in a much reduced order

## Slide 8: Possible ways to investigate H
Just plot every or some of the row of H.
  For example:
  It may show the rough tendency of evolution, but may be too busy when number of cycles increase
crank angle/ time
Deviation

## Slide 9: Possible ways to investigate H
-sum up every row of H to investigate the total deviation of every cycle. Associate every cycle with one value of deviation. The highest and lowest deviation cycles can be separated. High and low deviation cycles can be separated.
An example is shown below:
highest deviation cycle
lowest deviation cycle
A self-decided boundary to separate high and low deviation cycles

## Slide 10: Possible ways to investigate H
Track cycles with high deviation at the begining
example:
crank angle/ time
deviation
high deviation
low deviation
number of cycles
number of cycles
deviation
Initial crank angle, label the cycles with high deviation
See how the interesting cycles evolve until the final crank angle.

## Slide 11: Possible ways to investigate H
Compute transition probability
crank angle/ time
deviation
-Associate a transition probability distribution vector with every cluster except for the last crank angle

## Slide 12: Implementation on real data
Input data: TCCIII, Fired, Full View, image plane x=0, common grid id:S_2014_02_13_02
Clustering algorithm: kmeans
crank angles:
Number of cluster for each crank angle:

## Slide 13: Clusters

## Slide 14: Clusters

## Slide 15: Clusters

## Slide 16: Clusters

## Slide 17: Clusters

## Slide 18: Clusters

## Slide 19: Diagrams
Cycle 88 and 188 are randomly chosen. All the cycles can be visualized by a line pattern.

## Slide 20: Further interpretation
We will know cycle 88, for example, go through clusters 1-3-1-2-2-5

## Slide 21: Quantify deviation of centroids
-Every cluster is associated with a deviation value. Note the vertical axis change from cluster number to deviation.

## Slide 22: Quantify deviation of cycles
-Cluster transition process of a cycle is replaced by a deviation sequence.

## Slide 23: Overall view of quantification(Method 1 to investigate H)
-Both plots show the evolution of all cycles,
the first plot shows cluster transition, while
the second shows deviation sequence.
-In fact, the second plot contains all the information
about H (distance evolving matrix)

## Slide 24: Investigate H (Method 2)
Sum up every row of H and plot
highest deviation cycle #46
lowest deviation cycle #10
Threshold to separate high and low deviation cycles
High deviation cycles
Low deviation cycles

## Slide 25: Investigate H (Method 2)
See the deviation sequences of the highest and lowest deviation cycles.
Stay lowest
Never touches lowest

## Slide 26: Investigate H (Method 2)
-We can visualize highest and lowest deviation cycles and compare.

## Slide 27: Investigate H (Method 3)
Let's track cycles with high deviation at the beginning
-To find out whther high deviation at the beginning ends up with high deviation at the end
-If that is the case, the system could be unstable
-For this input data, that's not the case. None of the interesting cycles ends up with high deviation

## Slide 28: Investigate H (Method 4)
Let's compute every probability of transition between clusters
  In these cycles, they tend to transit to lower deviation. They may tend to go stable.

## Slide 29: Relate to pressure signal
Since high and low deviation cycles are separated (Method 2 to investigate H), it is possible to find out whether their corresponding pressure signals are also separated.
From these two sensors, we see the separation
of pressure signal is obvious

## Slide 30: Relate to pressure signal
-This sensor does not convey obvious separation between two groups of cycles.

## Slide 31: Relate to pressure signal
-From thse two sensors, separation of pressure
signals is also obvious.
-It may be true that for this system, large deviation
in pressure indicates large deviation in flow feature.

## Slide 32: Conclusion
An approach to simplify the description of similar cycles is proposed. It is realized by discretising time and clustering through flow features.
An idea to quantify deviation of flow features and cycles is derived afterwards. They are computed as distance between probability distributions.
Several methods to investigate the deviations are implemented, which may distinguish between high and low deviation cycles, reflect the tendency of variation and verify the stability of a system.
Pressure signals may indicate the deviation of flow features by studying regulation beforehand.